## Slide 1: XM MIPI Jig WOLVERINE Board
Application Department
Tim Lin, Brandy Liu
internal

## Slide 2: Outline
  Wolverine Structure
  Hardware Introduction
  Software Introduction
  Command List
  Instruction Format
  Command Description
  Program Introduction

## Slide 3: FPGA Structure

## Slide 4: Hardware Introduction

## Slide 5: Features
FPGA : Spartan6 LX45 CSG484
MIPI Bridge : SSD2828/SSD2828T 4Lane * 1
LDO : LD1117 adj * 2 support 1.2V~15V
RT4832 * 2(VSP*2 , VSN *2 , LEDA*2, LEDK*4)
Support SPI/CPU/I2C/RGB interface.
Support 16 bit GPIO.
Support VIN 5V~15V input
Onboard JTAG for FPGA program
Support USB power and adaptor supply.
Support offline function*.
*Offline function under development.

## Slide 6: Overview
MIPI interface Power for panel
Power for Backlight
SPI/CPU/I2C/RGB interface.
16bit GPIO voltage = VPNL_IO
Offline func. KEY
RESET func.
/RESET for Panel
USB_RESET for GL660
FPGA_RESET for FPGA
MIPI_RESET for SSD2828
LD1117 Adj
c

## Slide 7: Overview
FPGA reset mode select
0 : Global reset
1 : Keep RT4832 EN state (for ESD test use)
VPNL_IO and /RESET
output level select
1.8V : Adj by left resistor
2.8V : Adj by right resistor
Power input select
Left : adaptor (default)
Right : USB

## Slide 8: Overview
SD Card

## Slide 9: Overview
Note:
＊IO Voltage = VPNL_IO
1.General I/F
2./RESET,PWM0
3.GPIO
Suggestion
VPNL_IO -> LCM VDDIO
VDDIO -> LCM_VPNL

## Slide 10: Software Introduction

## Slide 11: When you Execute XmDisplayStudio
It will automatically create folders
Name | Description
Driver | Xm-Plus USB Controller Driver
Image | Test Pattern
Log | Log Data
Scope | Store Image from Oscilloscope
Script | Verification Script
EPP2USB_DLL_V12.dll | Xm-Plus Bridge Library
XMColoredLib.dll | Xm-Plus Richtextbox Libary

## Slide 12: Overview
1. Menu Strip
2. System Info
3.Image List
4.Active Bridge Info
2. Shortcut Area

## Slide 13: Overview
Area | Page | Item | Appendix
Menu Strip | File | About | About us
 |  | Exit | Exit Program
 | Project | Verification Page | Verification
 |  | AutoSet Page | Generate general interface
 |  | ManualSet Page | Read and Write Jig Register
 | Tool | USB Flash Edit Tool | Write/Read USB Control Flash
 |  | USB to EPP Command Edit | Write/Read Data to USB Control
 |  | Oscilloscope | Acquire Measurement Picture from Scope
 |  | Pattern_Gen_V13 | Generate Testing Pattern
 |  | SD Card_Control | Download Initial Code or Image into SDCard

## Slide 14: Overview
Area | Page | Item | Appendix
Menu Strip | Help | Script Command | Command Lists
 |  | INRUSH_CURRENT_RIPPLE_RELAY_BOARD | Relay Help
 | Item | Temperature Chamber | Testing Item
 |  | Source Measure | Testing Item
 |  | PWM Measure | Testing Item
 |  | Gamma Tool | Testing Item
 |  | MIPI LR SR TEST | Testing Item

## Slide 15: Overview (Verification Page)
2.Image List
When you switch the verification page…
1.System Info
7.Scan Instrument
10.Load Script from Active Page
3.Script Area
4.Message Area
6.Send Script from Active Page
9.Open Comm Port
8.Open or Cloase CA210 Device

## Slide 16: How to Use It?

## Slide 17: How to Use It?

## Slide 18: How to Use It?
File Name in Active Page
1.Add Sheet
2.Delete Sheet
3.Delete All Sheets
1.Selection Mode: User Selects part of Script
2.Normal Mode: Send from first Line to end line

## Slide 19: How to Use It?
1. Show: Send Test Pattern To Display
2. Download: Choose Image to Display
3. Preview: Preview the Image
4. Copy: Copy the File Name

## Slide 20: How to Use It?
Parameter | Description
SDCardGen | Please refer the “MicroSD Control_20181004.pptx”
Interface | Generate general interface for GUI Tool
Comment | Comment the “Mark” Code
UnComment | Uncomment the “Mark” Code
Parameter | Description
Send | Send the Script to Jig
Copy | Copy the Script
Clear | Clear the Textbox
Save As | Save the Script to the File
Paste | Paste the Script which copy from the other place

## Slide 21: How to Use It?
Parameter | Description
Copy | Copy the Script
Save as | Save the Script as Script
Clear | Clear the Textbox

## Slide 22: Command List

## Slide 23: Command List
Item | Instruction | Format
1 | fpga.set | Set XmPlus Wolverine Timing
2 | fpga.write | Write Data[] to set XmPlus Wolverine Jig
3 | fpga.read | Read Data[] from XmPlus Wolverine Jig
4 | bridge.write | Write Data[] To MIPI TX Bridge
5 | bridge.read | Read Data[] from MIPI TX Bridge
6 | gpio.dir | Set GPIO Direction, 0:Input 1:Output
7 | gpio.write | Set High Byte and Low Byte GPIO
8 | gpio.h.set | Write Data to the High Byte GPIO Port
9 | gpio.l.set | Write Data to the High Low GPIO Port
10 | gpio.read | Read Data from GPIO Data
11 | gpio.clr | Clear GPIO Status

## Slide 24: Command List
Item | Instruction | Format
12 | mipi.dsi | Set MIPI DSI Configure
13 | mipi.video | Set MIPI Video mode Parameter
14 | mipi.write | Send MIPI Packet
15 | mipi.read | BTA Request and Read Packet
16 | mipi.write.hs | Send High-Speed MIPI Packet
17 | mipi.read.hs | BTA Request and Read Packet
18 | mipi.bta | BTA Request
19 | mipi.ulp | MIPI Ultra Low Power
20 | image.fill | Display the Color by adjusting the 24-bit RGB Hex Value
21 | image.show | Display specific image name
image.write Display specific image name

## Slide 25: Command List (Instrument)
Item | Instruction | Format
22 | instr.define | Define Instrument to Alias Name
23 | instr.send | Send Data to Instrument
24 | instr.xfer | Send Data to Instrument and read data from Instrument
25 | Instr.read | Read data from Instrument
26 | Instr.close | Close Instrument

## Slide 26: Command List (System)
Item | Instruction | Format
27 | version | Read Software Version
28 | delay | Wait for milliseconds
29 | sleep | Wait for milliseconds
30 | scope.show | Call Scope Page to Use
31 | scope.save | Call Scope Method to Save Measure Graph
32 | pause | Stop the Script
33 | for | Repeat range between For and Endfor
34 | endfor | Repeat range between For and Endfor
35 | usb.cmd.write | Data[] must be even, Send Data to control XmPlus Platform
36 | txt.wrstr | Write String to File

## Slide 27: Command List (Power)
Item | Instruction | Parameter
37 | rt4832.0.write | Write Data to Control RT4832 0
38 | rt4832.2.write | Write Data to Control RT4832 2
39 | rt4832.0.read | Read Data from RT4832 0
40 | rt4832.2.read | Read Data from RT4832 2
41 | rt4832.0.vol | Set VSP and VSN Voltage to RT4832 0
42 | rt4832.2.vol | Set VSP and VSN Voltage to RT4832 2
43 | rt4832.0.bl | Set Backlight Single/Dual Mode Voltage to RT4832 0
44 | rt4832.2.bl | Set Backlight Single/Dual Mode Voltage to RT4832 2
45 | rt4832.0.lcd | LCD Enable to RT4832 0
46 | rt4832.2.lcd | LCD Enable to RT4832 2
47 | rt4832.0.led | LED Enable to RT4832 0
48 | rt4832.2.led | LED Enable to RT4832 2

## Slide 28: Command List (Power)
Item | Instruction | Parameter
49 | rt4832.0.delay | Time between VSP and VSN to RT4832 0
50 | rt4832.2.delay | Time between VSP and VSN to RT4832 2
51 | rt4832.0.set | Set VSP Voltage ,VSN Voltage ,Single/Dual to RT4832 0
52 | rt4832.2.set | Set VSP Voltage ,VSN Voltage ,Single/Dual to RT4832 2
53 | rt4832.0.bright | Set Brightness Value to RT4832 0
54 | Rt4832.2.bright | Set Brightness Value to RT4832 2

## Slide 29: Command List (Reset)
Item | Instruction | Parameter Format
55 | rst.en | reset control path, "0": external RC bottom, "1":FPGA internal s/w control
56 | rst.trigger | It Controled by D1 Time and D2 Time
57 | rst.pol | Trigger Type as below
58 | rst.set | Only Set D2 Time and Pol
59 | rst.reset | Trigger
It split into two groups
1. rst.en,rst.trigger, rst.pol
2. rst.set,rst.reset

## Slide 30: Command List (Comm Instrument)
Item | Instruction | Parameter Format
60 | ca210.xfer | Send Command and Read Data from CA210 , Store Data to Txt File
61 | ca210.send | Send Command
62 | ca210.read | Read Data from CA210
63 | comm.send | Send Command to Comm Port
64 | comm.xfer | Send Command Comm Port and Read Data from Comm Port
65 | comm.read | Read Data from Comm Port
66 | k80.flicker.read | Read Flicker Data from K80
67 | k80.bright.read | Read Bright Value from K80
68 | chamber.on | 
69 | chamber.off | 
70 | chamber.temp | 

## Slide 31: Command List (CPU Instrument)
Item | Instruction | Parameter Format
71 | cpu.addr.write | CPU Address Write
72 | cpu.data.write | CPU Data Write
73 | mcu.cs.h | CS To High
74 | mcu.cs.l | CS To Low

## Slide 32: Command List (SPI Instrument)
Item | Instruction | Parameter Format
75 | spi.set | Set SPI Mode Parameter
76 | spi.addr.write | SPI Address Write
77 | spi.data.write | SPI Data Write
78 | spi.cs.h | Set CS to Low voltage
79 | spi.cs.l | Set CS to high voltage

## Slide 33: Command List (I2C Instrument)
Item | Instruction | Parameter Format
80 | i2c.set | Set I2C Mode Speed
81 | I2c.addr | Set I2C Slave Address
82 | i2c.write | Write Data through I2C Interface
83 | i2c.read | Read Data from external Device through I2C Interface
84 | i2c.read.num | Set i2c read Number

## Slide 34: Command List(Special Device for General Interface )
Item | Instruction | Parameter Format
85 | dev.addr.mode | Set device memory mode
86 | dev.i2c.data.write | Write data for Specified Device through I2C Interface
87 | dev.i2c.addr.write | Write data for Specified Device through I2C Interface
88 | dev.rd | Read Data from Device
89 | dev.dummy.rd | Read Dummy Data from Device

## Slide 35: Instruction Format

## Slide 36: Command Format
Instruction | Format |  |  |  |  |  |  |  |  |  |  |  |  | 
fpga.set | Tx_Bank_En | EPP_EN |  | I/F_Mode1 |  | I/F_Mode2 |  |  |  |  |  | DCM_M |  | DCM_D
fpga.write | Address |  | Data |  |  |  |  |  |  | Data |  |  | Data | 
fpga.read | Address |  |  |  |  |  |  |  | Read Num |  |  |  |  | 
bridge.write | Address |  |  |  | Data |  |  |  |  |  | Data |  |  | 
bridge.read | Address |  |  |  |  |  | RdNum |  |  |  |  |  |  | 
gpio.dir | Gpio Direction |  |  |  |  |  |  |  |  |  |  |  |  | 
gpio.write | GpioHb |  |  |  |  |  |  | GpioLb |  |  |  |  |  | 
gpio.h.set | Data |  |  |  |  |  |  |  |  |  |  |  |  | 
gpio.l.set | Data |  |  |  |  |  |  |  |  |  |  |  |  | 
gpio.read |  |  |  |  |  |  |  |  |  |  |  |  |  | 
gpio.clr |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 37: Command Format
Instruction | Format |  |  |  |  |  |  |  |  |  |  |  |  |  | 
mipi.dsi | Lane Num |  |  |  | Speed |  |  |  | Mode |  |  |  |  |  | 
mipi.video | VLine | HPixels | Framerate |  |  | Vbp |  | Vfp |  | Hbp |  | Hfp | Vsync |  | Hsync
mipi.write | DCS Type |  |  |  |  |  |  |  | Data[] |  |  |  |  |  | 
mipi.read | Address |  |  |  |  |  |  |  | Read Number |  |  |  |  |  | 
mipi.write.hs | DCS Type |  |  |  |  |  |  |  | Data[] |  |  |  |  |  | 
mipi.read.hs | Address |  |  |  |  |  |  |  | Read Number |  |  |  |  |  | 
mipi.bta |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
mipi.ulp |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
image.fill | R |  |  | G |  |  | B |  |  |  | File.txt(Opt) |  |  | Para(Opt) | 
image.show | Image.bmp |  |  |  |  |  |  |  |  |  |  |  |  |  | 
image.write Image.bmp

## Slide 38: Command Format
Instruction | Format | 
instr.define | Instrument Addr | Alias
instr.send | Instrument Addr /Alias | Command
instr.xfer | Instrument Addr /Alias | Command
Instr.read | Instrument Addr /Alias | 
Instr.close | Instrument Addr /Alias | 

## Slide 39: Command Format
Instruction | Format |  |  | 
version |  |  |  | 
delay |  |  |  | 
sleep |  |  |  | 
scope.show |  |  |  | 
scope.save | Instrument/Alias Name |  | FileName.png | 
pause | Hint |  |  | 
For | Start | End | step | plus/minus
Endfor |  |  |  | 
usb.cmd.write | Data[] |  |  | 

## Slide 40: Command Format(RT4832)
Instruction | Parameter Format | 
rt4832.0.write | Register | Data
rt4832.2.write | Register | Data
rt4832.0.read | Register | Read Number
rt4832.2.read | Register | Read Number
rt4832.0.vol | VSP Voltage | VSN Voltage
rt4832.2.vol | VSP Voltage | VSN Voltage
rt4832.0.bl | Single/Dual | 
rt4832.2.bl | Single/Dual | 
rt4832.0.lcd | 0/1(disable/enable) | 
rt4832.2.lcd | 0/1(disable/enable) | 
rt4832.0.led | 0/1(disable/enable) | 
rt4832.2.led | 0/1(disable/enable) | 

## Slide 41: Command Format(RT4832)
Instruction | Parameter Format |  | 
rt4832.0.delay | [01]=1ms, [10]=2ms, [10]=5ms(delay time between VSP and VSN) |  | 
rt4832.2.delay | [01]=1ms, [10]=2ms, [10]=5ms(delay time between VSP and VSN) |  | 
rt4832.0.set | VSP Voltage | VSN Voltage | Single/Dual
rt4832.2.set | VSP Voltage | VSN Voltage | Single/Dual
rt4832.0.bright | 0/1(10bit/11bit) | Brightness Value(0~2047) | 
rt4832.2.bright | 0/1(10bit/11bit) | Brightness Value(0~2047) | 

## Slide 42: Command Format(Reset)
Instruction | Parameter Format | 
rst.en | 1/0 | 
rst.trigger | D1 Time | D2 Time
rst.pol | 1/0 | 
rst.set | D2 Time | 1/0
rst.reset |  | 

## Slide 43: Command Format(CA210,COMM)
Instruction | Parameter Format |  | 
ca210.xfer | Cmd | Delay | File.Txt
ca210.send | Cmd |  | 
ca210.read | File.Txt |  | 
comm.send | Data[] |  | 
comm.xfer | Data[] |  | 
comm.read |  |  | 
k80.flicker.read | File.Txt |  | 
k80.bright.read | File.Txt |  | 
chamber.on |  |  | 
chamber.off |  |  | 
chamber.temp | Temp |  | 

## Slide 44: Command Format(General Interface ,CPU)
Instruction | Parameter Format
cpu.addr.write | Cmd[]
cpu.data.write | Cmd[]
mcu.cs.h | No Parameter
mcu.cs.l | No Parameter

## Slide 45: Command Format(General Interface ,SPI)
Instruction | Parameter Format |  |  |  | 
spi.addr.write | Cmd[] |  |  |  | 
spi.data.write | Cmd[] |  |  |  | 
spi.cs.h | No Parameter |  |  |  | 
spi.cs.l | No Parameter |  |  |  | 
spi.set | CS | SckInv | RdDummy | WrClk | RdClk

## Slide 46: Command Format(General Interface ,I2C)
Item | Instruction | Parameter Format |  |  | 
71 | i2c.set | Clock “L” pulse width |  | Clock “H” pulse width | 
72 | I2c.addr | I2C Slave Address |  |  | 
73 | i2c.write | Data[] |  |  | 
74 | i2c.read | Read Data from external Device through I2C Interface |  |  | 
75 | i2c.read.num | Rd Cnt[20:16] | Rd Cnt[15:8] |  | Rd Cnt[7:0]

## Slide 47: Special Device for General Interface
Instruction | Parameter Format
dev.addr.mode | Cmd
dev.i2c.addr.write | Cmd[]
dev.i2c.data.write | Data[]
dev.rd | FileName.txt
dev.dummy.rd | FileName.txt
dev.addr.mode: Set memory addressing mode
00b: Horizontal Addressing Mode
01b: Vertical Addressing Mode
10b: Page Addressing Mode
11b: Invalid

## Slide 48: Command Description

## Slide 49: fpga.set
fpga.set Pll_Bank_En EPP_EN I/F_Mode1 I/F_Mode2 DCM_M DCM_D
Description: Write Data to Set Jig interface and timing
Parameter | Description
Tx_Bank_En | SSD2828 Bank Enable and Mode Set P[0]:Bank 0 SSD2828 Enable P[1]:Bank 0 SSD2828 Mode, 0:Command Mode, 1:Video Mode P[4]:Bank 2 SSD2828 Enable P[5]:Bank 2 SSD2828 Mode, 0:Command Mode, 1:Video Mode
EPP_EN | P[0]:Bank 0 SSD2828 EPP wr/rd, 0:disable, 1:enable P[4]:Bank 2 SSD2828 EPP wr/rd, 0:disable, 1:enable
I/F_Mode1 | P[5:3] 000:I80 Interface 001:M68 Interface 010:RGB Interface 011:SPI Interface 100:I2C Interface 101:I2c+RGB Interface P[2:0] 000 : SPI 3wire/4wire, write/read 8bit 001 : SPI 3wire, write 9bit/read 8bit 010 : RGB(HS/VS+DE) + SPI 3wire/4wire, write/read 8bit 011 : RGB(HS/VS+DE) + SPI 3wire, write 9bit/read 8bit 100 : RGB(HS/VS) + SPI 3wire/4wire, write/read 8bit 101 : RGB(HS/VS) + SPI 3wire, write 9bit/read 8bit 110 : RGB(DE) + SPI 3wire/4wire, write/read 8bit 111 : RGB(DE) + SPI 3wire, write 9bit/read 8bit

## Slide 50: fpga.set
Receive Data: None
Example:
fpga.set 0x33 0x11 0x13 0xff 67 60
Parameter | Description
I/F_Mode2 | P[7:4] : RGB mode => interface bits define P[3] : mp , Mclk polarity set P[2] : ep , Enable(DE) polarity set P[1] : hsp , Hsync polarity set P[0] : vsp , Vsync polarity set
DCM_M | Jig Frequency= 60(M) * DCM_M / DCM_D
DCM_D | 

## Slide 51: fpga.write
fpga.write RegAddr Data0 Data1 Data2
Description: Write Data to the Jig Register
Parameter:
Receive Data: None
Example:
fpga.write 0xfb 0xff
Parameter | Description
Reg Addr | Register Address(1-Byte) -> 0x
Data | Register Value(2-Btye) -> 0x , 0x , …

## Slide 52: fpga.read
fpga.read Register ReadNum
Description: Read Several Data from the Jig
Parameter: Register Address
Example:
fpga.read 0xfb 1
Parameter | Description
Register | Register Address(1-Byte)
ReadNum | Count of readings from Jig

## Slide 53: bridge.write
bridge.write RegAddr Data
Description: Write Data to the MIPI TX Bridge Chip(SSD2828)
Parameter:
Receive Data: None
Example: bridge.write 0xc9 0x1c 0x07
Parameter | Description
RegAddr | Register Address(1-Byte) -> 0x
Data | Register Value(2-Btye) -> 0x , 0x

## Slide 54: bridge.read
bridge.read Register ReadNum
Description: Read Data from the MIPI TX Bridge Chip(SSD2828)
Parameter: Register Address
Parameter | Description
Register | Register Address(1-Byte)
Read Num | Count of readings from the Mipi Tx Bridge
Example:
bridge.read 0xb0 2

## Slide 55: gpio.dir
gpio.dir gpiodir
Description: Set GPIO input / output direction
Parameter:
DirHB: Set HB GPIO Direction, Input: 0 , Output:1
DirLB : Set LB GPIO Direction, Input: 0 , Output:1
Receive Data: None
Example:
gpio.dir 0x11
GPIO Input/Output Direction Set |  |  |  |  |  |  | 
B[7] | B[6] | B[5] | B[4] | B[3] | B[2] | B[1] | B[0]
0 | 0 | 0 | DirHB | 0 | 0 | 0 | DirLB
HB
LB

## Slide 56: gpio.write
gpio.write gpiohb gpiolb
Description: Set GPIO output
Parameter:
Receive Data: None
Example:
  gpio.write 0x80 0x01
GPIO |  |  |  |  |  |  |  | 
 | B[7] | B[6] | B[5] | B[4] | B[3] | B[2] | B[1] | B[0]
HB | R15 | R16 | R17 | R19 | P15 | P16 | P17 | P18
LB | V17 | V18 | V19 | V20 | T17 | T18 | T19 | T20
P17
P18
P15
P16
R17
R19
R15
R16
T19
T20
T17
T18
V19
V20
V17
V18
HB
LB

## Slide 57: gpio.h.set
gpio.h.set gpio
Description: Set GPIO(HB) output
Parameter:
Receive Data: None
Example:
    gpio.h.set 0xA1
GPIO |  |  |  |  |  |  |  | 
 | B[7] | B[6] | B[5] | B[4] | B[3] | B[2] | B[1] | B[0]
HB | R15 | R16 | R17 | R19 | P15 | P16 | P17 | P18
P17
P18
P15
P16
R17
R19
R15
R16
HB

## Slide 58: gpio.l.set
gpio.l.set gpio
Description: Set GPIO LB Output
Parameter:
Receive Data: None
Example:
  gpio.l.set 0x85
GPIO |  |  |  |  |  |  |  | 
 | B[7] | B[6] | B[5] | B[4] | B[3] | B[2] | B[1] | B[0]
LB | V17 | V18 | V19 | V20 | T17 | T18 | T19 | T20
T19
T20
T17
T18
V19
V20
V17
V18
LB

## Slide 59: gpio.read
gpio.read
Description: Read GPIO Status
Parameter: No Parameter
Example:
gpio.read

## Slide 60: gpio.clr
gpio.clr
Description: Clear GPIO Status
Parameter: No Parameter
Receive Data: None
Example:
  gpio.clr

## Slide 61: mipi.dsi
mipi.dsi Lane DataRate Mode
Description: Set MIPI DSI Configuration
Parameter:
Receive Data: None
Example:
mipi.dsi 2 1000 burst
Parameter | Description
Lane | The Number of Data Lane (1¦2¦3¦4)
DataRate | High Speed data rate per lane in Mbps unit(Mbps/Lane)
Mode | burst,syncevent,syncpluse

## Slide 62: mipi.video
mipi.video vline hPixels framerate vbp vfp hbp hfp vsync hsync
Description: Set MIPI video mode parameter
Example:
mipi.video 1334 750 60 4 540 30 2 3 6
Parameter | Description
vLine | Active vertical display lines per frame
hPixels | Active horizontal display pixels per line
Framerate | Frame rate, fixed value is 60
Vbp | Vertical back porch lines
Vfp | Vertical front porch lines
Hbp | Horizontal back porch
Hfp | Horizontal front porch
Vsync | Vertical sync pluse width
hsync | Horizontal sync pluse width

## Slide 63: mipi.write
mipi.write di parm1 parm2 …
Description: Send MIPI short or long packets in low power mode
Example:
mipi.write 0x23 0x00 0x00
Parameter | Description
di | 0x03: Generic SHORT WRITE , no parameter 0x13: Generic SHORT WRITE , 1 parameter 0x23: Generic SHORT WRITE , 2 parameter 0x05: DCS SHORT WRITE , no parameter 0x15: DCS SHORT WRITE , 1 parameter 0x39: DCS Long WRITE
Parm1 | Parameter 1 for DCS Packet
Parm2 | Parameter 2 for DCS Packet

## Slide 64: mipi.read
mipi.read RegAddr ReadNum
DI WC_LSB WC_MSB ECC Data0 Data1 CRC_LSB CRC_MSB
DI data0 data1 ECC
Description: Request BTA and read MIPI packet in low power mode
Parameter:
Receive Data: any bytes of MIPI packet data
Example:
mipi.read 0x0a 1
Parameter | Description
Register | Register Address
ReadNum | Count of readings from the LCD Display Driver

## Slide 65: mipi.write.hs
mipi.write.hs di parm1 parm2 …
Description: Send MIPI short or long packets in high speed mode
Receive Data: None
Parameter | Description
di | 0x03: Generic SHORT WRITE , no parameter 0x13: Generic SHORT WRITE , 1 parameter 0x23: Generic SHORT WRITE , 2 parameter 0x05: DCS SHORT WRITE , no parameter 0x15: DCS SHORT WRITE , 1 parameter 0x39: DCS Long WRITE
Parm1 | Parameter 1 for DCS Packet
Parm2 | Parameter 2 for DCS Packet

## Slide 66: mipi.read.hs
mipi.read.hs RegAddr ReadNum
Description: Request BTA and Read MIPI Packet in High Speed Mode
Parameter:
Receive Data: any bytes of MIPI packet data
Parameter | Description
Register | Register Address
ReadNum | Count of readings from the LCD Display Driver

## Slide 67: mipi.bta
mipi.bta
Description: Request BTA
Parameter: None
Receive Data: None
Appendix: only for Verification

## Slide 68: mipi.ulp
mipi.ulp
Description: Set the MIPI TX Bridge to Ultra Low Power Mode
Parameter: None
Receive Data: None
Appendix: Only for Verification

## Slide 69: image.fill
image.fill 8bit_R 8bit_G 8bit_B FileName.txt
Description: Can be display the color by adjust the 24bit RGB Value
Parameter:
Parameter | Description
8bit_R | Red Color , 0~255
8bit_G | Green Color , 0~255
8bit_B | Blue Color , 0~255
FileName.txt | (Optional) Store the File Name, Default Path is under Log directory

## Slide 70: image.fill
Receive Data: None
Example :
if You want to display :
Red Color: image.fill 255 0 0
Green Color: image.fill 0 255 0
Blue Color: image.fill 0 0 255
  If you want to display and record it:
image.fill 252 252 252 gamma.txt

## Slide 71: image.write
image.write Name
Description: Display specific image name
Parameter: Image FileName
Receive Data: None
Example:
Image.write GirlBoys.bmp
Parameter | Description
Name | Support png and bmp format

## Slide 72: image.show
image.show Name
Description: Display specific image name
Parameter: Image FileName
Receive Data: None
Example:
Image.show GirlBoys.bmp
Parameter | Description
Name | Support png and bmp format

## Slide 73: instr.define
instr.define Instrument Alias_Name
Description: Define simple names to replace difficult and long names
Parameter:
Receive Data: None
Example:
  instr.define USB0::0x2A8D::0x0101::MY57505581::INSTR Meter
  ＊Please Refer to Appendix Instrument Connection for details
Parameter | Description
Instrument | Real Instrument Name in Keysight IO Libary
Alias Name | Alias Name named by yourself

## Slide 74: instr.send
instr.send Instrument Instruction
Description: Send Instruction to Instrument
Parameter:
Parameter | Description
Instrument | Instrument Name or Alias Name
Instruction | Send Instruction to Instrument
Receive Data: None
Example:
instr.define USB0::0x2A8D::0x0101::MY57505581::INSTR Meter
instr.send Meter *CLS
＊*CLS is Command of Keysight Meter and it will clear instrument status
＊Please Refer to Appendix Instrument Connection for details

## Slide 75: instr.read
instr.read Instrument Filename.txt
Description: Read Data from Instrument
Parameter:
Parameter | Description
Instrument | Instrument Name or Alias Name
Instruction | Send Instruction to Instrument
FileName.txt | (Optional) Save Data to Filename.txt
Example:
instr.define USB0::0x2A8D::0x0101::MY57505581::INSTR Meter
instr.send Meter *IDN?
instr.read Meter
Read[3]: Keysight Technologies,34465A,MY57505581,A.02.17-02.40-02.17-00.52-03-01
＊Please Refer to Appendix Instrument Connection for details

## Slide 76: instr.xfer
instr.xfer Instrument Instruction filename.txt
Description: Send Instruction and Read from Instrument
Parameter:
Parameter | Description
Instrument | Instrument Name or Alias Name
Instruction | Send Instruction to Instrument
FileName.txt | (Optional) Save Data to FileName.txt
Example:
instr.define USB0::0x2A8D::0x0101::MY57505581::INSTR Meter
instr.xfer Meter *IDN?
Read[2]: Keysight Technologies,34465A,MY57505581,A.02.17-02.40-02.17-00.52-03-01
＊Please Refer to Appendix Instrument Connection for details

## Slide 77: instr.close
instr.close Instrument
Description: Close the Instrument and clean handler
Parameter:
Parameter | Description
Instrument | Instrument Name or Alias Name
Receive Data: None
Example:
instr.define USB0::0x2A8D::0x0101::MY57505581::INSTR Meter
instr.xfer Meter *IDN?
instr.close Meter
＊Please Refer to Appendix Instrument Connection for details

## Slide 78: version
version
Description: Read XmDisplay Studio Version
Parameter: None
Receive Data: A.B.C.D
Data | Description
A | Major Version
B | Minor Version
C | Build number
D | Revision

## Slide 79: delay
delay milliseconds
Description: Wait for the amount of time, in milliseconds
Parameter: the amount of time , in milliseconds
Receive Data: None
Example:
delay 100

## Slide 80: sleep
sleep milliseconds
Description: Wait for the amount of time, in milliseconds
Parameter: The amount of time , in milliseconds
Receive Data: None
Example:
sleep 100

## Slide 81: scope.show
scope.show
Description: Retrieve the Measuring Image form Oscilloscope
Parameter: None
Receive Data: None
＊It will find out the all Oscilloscope Device

## Slide 82: scope.save
scope.save Instrument ImageName.png
Description: Retrieve the Measuring Image form Oscilloscope and
Save the Image
Parameter:
Parameter | Description
Instrument | Instrument Name or Alias Name
ImageName.png | Save Image FileName.png and store in scope folder.
Receive Data: None
Example:
instr.define USB0::0x0957::0x17A0::MY52160518::INSTR MsoScope
scope.save MsoScope a.png

## Slide 83: pause
pause Hint
Description: stop and pause the program
Parameter:
Parameter | Description
Hint | It will show the “hint” on the Messagebox
Receive Data: None
Example:
pause StopToMeasure

## Slide 84: for
for Initializer Ending Step Iterator
Description: Repeat to Execute the range of ‘for’ to ‘endfor’
Parameter:
Parameter | Description
Initializer | Start Value
Ending | Ending Value
Step | Step , plus or minus It is like “Step++” or “Step --”
iterator | 
Receive Data: None
Example:
for 0 4 1 plus (for(i=0;i<4;i++))

## Slide 85: endfor
endfor
Description: Repeat to Execute the range of ‘for’ to ‘endfor’
Parameter: None
Example:
for 0 256 1 plus
mipi.write.hs 0x23 0x00 0x9b
mipi.write.hs 0x23 0xd4 reg
endfor
Sudo Code:
for (i=0,i< 256;i++)
{
mipi.write.hs 0x23 0x00 0x9b
mipi.write.hs 0x23 0xd4 i
}
＊It can use “reg” to replace the value within the Rage of ‘for’ and ‘endfor’

## Slide 86: usb.cmd.write
usb.cmd.write Data[]
Description: Send Data to control XmPlus Platform
Parameter:
Parameter | Description
Data[] | Data[] must be even, Send Data to control Jig Platform It shortens the time among commands
Receive Data: None
Example:
usb.cmd.write 0xfc 0xff

## Slide 87: txt.wr
txt.wr Parameter Filename.txt
Description: Save Parameter to FileName.txt
Parameter:
Parameter | Description
Parameter | /n: Next Line /t: Add ‘Tab’ /s: Add ‘Space’
Filename.txt | FileName.txt
Receive Data: None
Example:
txt.wr \n a.txt

## Slide 88: rt4832.0.write
rt4832.0.write Register Data
Description: Write Data to RT4832 NO. 1
Parameter:
Parameter | Description
Register | RT4832 Register
Data | Send the Data to RT4832 Register
Receive Data: None
Example:
rt4832.0.write 0x02 0x30

## Slide 89: rt4832.0.read
rt4832.0.read Register RdNum
Description: Read Data from RT4832 NO. 1 Register
Parameter:
Parameter | Description
Register | RT4832 Register
RdNum | Number of reading RT4832 Register
Example:
rt4832.0.read 0x01 2
Read[1]: 0x06

## Slide 90: rt4832.0.vol
rt4832.0.vol VSP VSN
Description: Set VSP and VSP Voltage
Parameter:
Parameter | Description
VSP | Set the VSP Voltage, Register Address is 0x0e in RT4832
VSN | Set the VSN Voltage, Register Address is 0x0f in RT4832
Receive Data: None
Example:
rt4832.0.vol 5.5 -5.5

## Slide 91: rt4832.0.bl
rt4832.0.bl PowerMode
Description: Set the Back Light Dual Mode or Singe Mode
Parameter:
Parameter | Description
PowerMode | Dual / Single Mode Register Address is 0x0A in RT4832
Receive Data: None
Example:
rt4832.0.bl dual

## Slide 92: rt4832.0.lcd
rt4832.0.lcd Enable
Description: Enable LCD Power with RT4832 No.0
Parameter:
Parameter | Description
Enable | Enable the LCD Power With RT4832 NO. 0 0:Disable 1:Enable Register Address is 0x0C in RT4832
Receive Data: None
Example:
rt4832.0.lcd 1

## Slide 93: rt4832.0.led
rt4832.0.led Enable
Description: Enable Back Light with No.0 RT4832
Parameter:
Parameter | Description
Enable | Enable the Back Light With RT4832 NO. 0 0:Disable 1:Enable Register Address is 0x0A in RT4832
Receive Data: None
Example:
rt4832.0.led 1

## Slide 94: rt4832.0.delay
rt4832.0.delay Time
Description: Delay time between VSP and VSN
Parameter:
Parameter | Description
Time | Delay Tim Between VSP and VSN 0=No Constraint,1=1ms, 2=2ms, 3=5ms Register Address is 0x0D in RT4832
Receive Data: None
Example:
rt4832.0.delay 3

## Slide 95: rt4832.0.set
rt4832.0.set VSP VSN Mode
Description: Set VSP , VSN voltage and Back Light Mode
Parameter:
Receive Data: None
Example:
rt4832.0.vol 5.5 -5.5 Dual
Parameter | Description
VSP | Set the VSP Voltage, Register Address is 0x0e in RT4832
VSN | Set the VSN Voltage, Register Address is 0x0f in RT4832
Mode | Dual / Single Mode

## Slide 96: rt4832.0.bright
rt4832.0.set Mode Value
Description: Set Brightness Value to No. 0 RT4832
Parameter:
Parameter | Description
Mode | 0/1(10bit/11bit)
Value | Brightness Value(0~2047)
Receive Data: None
Example:
rt4832.0.bright 1 1024

## Slide 97: rst.en
rst.en mode
Description: reset control path
Parameter:
Parameter | Description
mode | 0: external RC bottom, 1:FPGA internal s/w control
Receive Data: None
Example:
rst.en 1

## Slide 98: rst.pol
rst.pol mode
Description: Trigger Polarity
Parameter:
Receive Data: None
Example:
rst.en 1
rst.pol 0

## Slide 99: rst.trigger
rst.trigger D1Time D2Time
Description:
1. It is controlled by D1 and D2 Time
2. It will reset automatically.
Parameter:
// pol :"0" __ ____________
// SRST ____| |____|
// delay d1 d2
//
// pol :"1"
// ____ ____
// SRST |__| |_____________
// delay d1 d2
Receive Data: None
Example:
rst.en 1
rst.pol 0
rst.trigger 0xff 0xff
＊ D1 Time = 100ns*255 = 25.6us, D2 Time =100 ns*256 = 25.6us, Appendix A

## Slide 100: rst.set
rst.set D2Time Polarity
Description:
It is only controlled by D2 Time and Polarity
Parameter:
// pol :"0" __ ____________
// SRST ____| |____|
// delay d1 d2
//
// pol :"1"
// ____ ____
// SRST |__| |_____________
// delay d1 d2
Receive Data: None
Example:
rst.set 0xff 0
rst.reset
＊Refer to Appendix B

## Slide 101: rst.reset
rst.reset
Description: It will reset automatically.
Parameter: None
Receive Data: None
Example:
                rst.set 0xff 0
                rst.reset
＊ rst.set and rst.reset are paired and cannot be used alone

## Slide 102: ca210.send
ca210.send Command
Description: Send Command to CA210
Parameter:
Parameter | Description
Command | Send Command to KONICA CA210
Receive Data: None
Example:
ca210.send MES
＊Please Refer to Appendix CA-210 Connection for details

## Slide 103: ca210.read
ca210.read FileNam.txt
Description: Read Data from CA210
Parameter: None
Example:
ca210.read a.txt
＊Please Refer to Appendix CA-210 Connection for details
Parameter | Description
FileNam.txt | (Optional)Store the File Name, Default Path is under Log directory

## Slide 104: ca210.xfer
ca210.xfer Cmd Time FileName.txt
Description:
Send Command and Read Data from CA210 , Store Data to Txt File
Parameter:
Parameter | Description
Cmd | CA210 Command
Time | Delay Time(Millisecond) Between Sending Command and Reading Data
FileName.txt | (Optional)Store the File Name, Default Path is under Log directory
Example:
ca210.xfer MES 200 NL gamma.txt (Send MES instruction, read data after 200 ms)
＊Please Refer to Appendix CA-210 Connection for details

## Slide 105: comm.send
comm.send Command
Description: Send Command Over Serial Port
Parameter:
Parameter | Description
Command | Send Command to Instrument over the Serial Port
Receive Data: None
Example:
comm.send MES

## Slide 106: comm.read
comm.read
Description: Read Data from Instrument over the Serial Port
Parameter: None
Example:
comm.read

## Slide 107: comm.xfer
Example:
comm.xfer Command
comm.xfer Command
Description:
Send Command and Read Data from Instrument over the Serial Port
Parameter:
Parameter | Description
Command | Instrument Command

## Slide 108: k80.bright.read
k80.bright.read FileName.txt
Description:
Read Bright Data from K80 and Store Data to Txt File
Parameter:
Parameter | Description
FileName.txt | (Optional) Store the File Name, Default Path is under Log directory
Example:
k80.bright.read bright.txt (read data and Save Data to bright.txt)

## Slide 109: k80.flicker.read
k80.flicker.read FileName.txt
Description:
Read Data from K80 and Store Data to Txt File
Parameter:
Parameter | Description
FileName.txt | (Optional) Store the File Name, Default Path is under Log directory
Example:
k80.flicker.read flicker.txt

## Slide 110: chamber.on
chamber.on
Description:
Open the Chamber
Parameter:None

## Slide 111: chamber.off
chamber.ff
Description:
Close the Chamber
Parameter:None

## Slide 112: chamber.temp
chamber.temp temperature
Description:
Set the Chamber temperature
Parameter: temperature

## Slide 113: cpu.addr.write
cpu.addr.write command []
Description:
Send Command through CPU Interface
Parameter:
Parameter | Description
Command[] | commands
Example:
cpu.addr.write 0x8d 0x14 0xA1 0xC8 0xAF

## Slide 114: cpu.data.write
cpu.data.write command []
Description:
Send data through CPU interface
Parameter:
Parameter | Description
Command | Data[]
Example:
cpu.data.write 0xff

## Slide 115: mcu.cs.h
mcu.cs.h
Description:
/CS to High
Parameter: no parameter
Example:
mcu.cs.h

## Slide 116: mcu.cs.l
mcu.cs.l
Description:
/CS to Low
Parameter: no parameter
Example:
mcu.cs.l

## Slide 117: spi.set
spi.set cs spisckinv rddmyclk spiwrclkh spiwrclkl
Description:
Set SPI timing and function
Parameter:
Parameter | Description
cs | 0:Control by CS bit, 1:Internal module Cycle
spisckinv | 0: SCK Low, Rising Edge latch Data 1: SCK High , falling edge latch data
rddmyclk | 0:no dummy clk 1: with dummy clk
spiwrclkh | write Clk “L” pulse width
spiwrclkl | write Clk “H” pulse width

## Slide 118: spi.addr.write
spi.addr.write parm[]
Description:
Send Command through SPI interface
Parameter:
Parameter | Description
Parm | Data[]

## Slide 119: spi.data.write
spi.data.write parm[]
Description:
Send Command through SPI interface
Parameter:
Parameter | Description
Pram | Data[]

## Slide 120: spi.cs.h
spi.cs.h
Description:
Control CS Pin to High Voltage
Parameter: No Parameter
Example:
  spi.cs.h

## Slide 121: spi.cs.l
spi.cs.l
Description:
Control CS Pin to Low Voltage
Parameter: No Parameter
Example:
  spi.cs.l

## Slide 122: i2c.set
i2c.set i2c_sckh i2c_sckl
Description:
Set I2C Speed
Parameter:
Parameter | Description
i2c_sckh | i2c sck “H” pluse clk number
i2c_sckl | i2c sck “L” pluse clk number
Example:
i2c.set 0x32 0x32

## Slide 123: i2c.addr
i2c.addr slaveaddr
Description:
Set I2C Timing and Speed
Parameter:
Parameter | Description
slaveaddr | I2C Slave Address
Example:
i2c.addr 0x78

## Slide 124: i2c.write
i2c.write parms[]
Description:
Write parms[] through I2C Interface
Parameter:
Parameter | Description
Parms[] | Data[]
Example:
i2c.write 0x78 0x87

## Slide 125: i2c.read
i2c.read
Description:
Read Data from Device through I2C Interface
Parameter: No Parameter

## Slide 126: i2c.read.num
i2c.read.num Rd_H Rd_L
Description:
Set Read Number for I2C
Parameter:
Parameter | Description
Rd_H | I2C Read Num High Byte
Rd_L | I2C Read Num Low Byte
Example:
i2c.read.num 0x12 0x34(0x1234,4660)

## Slide 127: dev.addr.mode
dev.addr.mode mode
Description:
Set Memory Addressing Mode
Parameter:
Parameter | Description
Mode | 00b: Horizontal Addressing Mode 01b: Vertical Addressing Mode 10b: Page Addressing Mode 11b: Invalid

## Slide 128: dev.i2c.addr.write
dev.i2c.addr.write command[]
Description:
Write Data to Specified Device(XUA003) through I2C Interface
Parameter:
Parameter | Description
Command[] | Data[]
Example:
dev.i2c.addr.write 0x12 0x34

## Slide 129: dev.i2c.data.write
dev.i2c.data.write command[]
Description:
Write Data to Specified Device(XUA003) through I2C Interface
Parameter:
Parameter | Description
Command[] | Data[]
Example:
dev.i2c.data.write 0x12 0x34

## Slide 130: dev.rd
dev.rd filename.txt
Description:
Read Data from Device
Parameter:
Parameter | Description
Filename.txt | (Optional) Save Data to Filename.txt
Example:
dev.rd a.txt
dev.rd

## Slide 131: dev.dummy.rd
dev.dummy.rd filename.txt
Description:
Read Dummy Data from Device
Parameter:
Parameter | Description
Filename.txt | (Optional) Save Data to Filename.txt
Example:
dev.dummy.rd a.txt
dev.dummy.rd

## Slide 132: Program Introduction

## Slide 133: Program Infrastructure
Directory | Document | Description
Main | About.cs | 
 | Comport_Form.cs | Serial Port Setting Page
 | ExpandFpag_Form.cs | Jig Write/Read Reg Page
 | Help_Form.cs | Introduce Instruction Page
 | InterfaceSetting_Form | Interface Process Setting
 | MainSetting_From.cs | Main Page
 | SDCardControl_Form.cs | Write/Read SdCard Control
 | Scope_Form.cs | Oscilloscope Page
 | ScriptSetting_Form.cs | Control Driver Page
 | Source_Measure.cs | Measure Source Page
 | TemperatureTest.cs | High and low temperature test
 | XmGammaTool | GammaTest

## Slide 134: Program Infrastructure
Directory | Document | Description
Comm | XM_Comm.cs | Base Class
 | XM_Comm_IO.cs | Inheritance XM_Comm, only for SDCardCtrl
 | XM_Comm_USB.cs | Inheritance XM_Comm, only for General Control
 | XM_Cpu.cs | Testing Code, Not Use
 | XM_Rgb.cs | Testing Code, Not Use
 | XM_Visa32.cs | Visa Library for Instrument

## Slide 135: Program Infrastructure
Directory | Document | Description
XmComm | XM_Cmd_Lib.cs | Build up Xm-Plus Command Structure
 | XM_ExeCmd.cs | Base Class for Deal With Jig Command
 | XM_ExeCommCmd.cs | Inheritance Class for Execute Series Port Instruction
 | XM_ExeEquipCmd.cs | Inheritance Class for Execute Equiptment Instruction
 | XM_ExeMainCmd.cs | Library for Classify the Instruction
 | XM_ExeSysCmd.cs | Inheritance Class for Execute System Instruction
 | XM_ExeWol_Util.cs | Utility for Mipi Tx Bridge function
 | XM_ExeWolCmd_Util.cs | Inheritance Class for Execute LCD Display Driver Command

## Slide 136: Program Infrastructure
Directory | Document | Description
StudioUtil | XM_Bridge_Flash.cs | Bridge Flash Utility
 | XM_Bridge_Util.cs | API for Search Bridge (Timer)
 | XM_Digital_Util.cs | API for Format interchange(string <-> int, double,float)
 | XM_Equip_Util.cs | API for Control Equipment
 | XM_HidUtil.cs | Testing Code, Not Use
 | XM_Img_Lib.cs | API for Image
 | XM_Ini_Util.cs | API for INI Control (Record Data to INI File)
 | XM_IO_Util.cs | API for File IO Control
 | XM_Log_Util.cs | API for Log System Message
 | XM_Mipi_Util.cs | API for Control Mipi Tx Bridge
 | XM_Param_Util.cs | API for Update and Control Jig(Not Use)
 | XM_SDCard_Util.cs | API for SDCard IO Control
 | XM_Sytem_API.cs | Windows API

## Slide 137: Library
FastColoredTextbox is used to indicate the color of the text

## Slide 138: Data Structure
public class XmPlusCmd
{
public string Cmd { get; set; } //Command
public byte Type { get; set; } //Command Type，R/W/WR/Found/Save
public int MaxParm { get; set; } //Parameter Count
public int MaxValue { get; set; } //Max Value
public byte Category { get; set; }
public byte Class { get; set; }
public byte Reg { get; set; } //Register
public int Delay { get; set; } //Delay Time for Next Operation
public ArrayList Item { get; set; } //Fixed Item
}
Class:
0: Comm Command
1: System Command
2: Instrument Command
3. XmPlus Command
4. For Command
5. CA-210 Command
Category :
0: No Parameter
1: Examine Parameter as String
2: Examine Parameter as Numeric
3: Examine Parameter as Numeric and Parameter Num Equal
4. Examine Parameter as String and Parameter Num Equal
5: Examine the last One Item (String,DSI)
6: Examine the last One Item (String,For) and compare value
7. Examine the last one Item as txt file
8: Examine Parameter as Float and the last one is negative
9. Examine Parameter as Reg(Numeric) and Parameter Num Equal
10. Examine Parameter as Reg and the last one Item as txt file
11. Examine Parameter as Reg, The last second as TxtFormat, and the last one Item as txt file

## Slide 139: Data Structure
public class ScriptInfo
{
public string Cmd { get; set; } //Command
public string CleanCmd{ get; set; } //Clean Command
public int Index { get; set; } //Command Option among array
public byte Result { get; set; }
public string Msg{ get; set; } //Appendix
public string Line{ get; set; } //Rows
}
public class XmResult
{
public string XmPlusCmd { get; set; } //Command
public int Line { get; set; }
public int End { get; set; }
public bool Result { get; set; } //Check if the format
public XmResult(string XmPlusCmd, int Line, int End, bool Result)
{
this.XmPlusCmd = XmPlusCmd;
this.Line = Line;
this.End = End;
this.Result = Result;
}
}

## Slide 140: Program Structure
ScriptSetting_Form.cs
XM_ExeMainCmd.cs
XM_ExeCommCmd_Util
XM_ExeEquipCmd_Util
XM_ExeSysCmd_Util
XM_ExeForCmd_Util
XM_ExeWolCmd_Util
Using
1.Comm Device
2.CA210 Device
Using
1.Instrument Control
Support
1.System Command
Using
1.For ,EndFor
Using
1.Only For Jig Control

## Slide 141: Main Program
private void SendXmCmd()
{
string[] CmdLines = null;
bool ret = true, bAllCmd = true;
string ErrInfo = null;
List<ScriptInfo> lScriptInfo = new List<ScriptInfo>();
FastColoredTextBox FastRichBox = (FastColoredTextBox)tctl_pages.TabPages[tctl_pages.SelectedIndex].Controls["FastColoredText"];
/*Verify USB Connection*/
if (!ExeStatus(FastRichBox)) { MessageBox.Show("Stop Running!"); return; }
/*Selection or All*/
CmdLines = WorthXmCmd(FastRichBox, ref bAllCmd).Split(DelimiterChars[4]);
/*Verify and Exam Command*/
ErrInfo = ExeCmd.ExamScript(CmdLines, lScriptInfo);
/*Deal With Error And Present*/
if (bAllCmd && !DealWithXmCmds(FastRichBox, ref lScriptInfo)) { FastRichBox.Focus(); ret = ShowContinueDialog(); }
if (Setting.CmdMsg) rtf_ElecsMsg.Text = ErrInfo;

## Slide 142: Main Program
if (ret) // Check if the format is true or false
{
XmCmd XMCmds = new XmCmd(lScriptInfo);
XmThead = new Thread(new ParameterizedThreadStart(Run))
{
IsBackground = true
};
XmThead.Start(XMCmds); //Start Thread
}
else
ExeStatus(FastRichBox);
}

## Slide 143: Main Program
public bool ExcuteCmd( string Command, XmPlusCmd XmPlus, ref string RdStr)
{
bool ret = true;
if (XmPlus.Class == 0) ret = DealWithComm(Command, XmPlus, ref RdStr);
if (XmPlus.Class == 1) ret = DealWithSystem(Command, XmPlus, ref RdStr);
if (XmPlus.Class == 2) ret = DealWithEquip(Command, XmPlus, ref RdStr);
if (XmPlus.Class == 3) ret = DealWithWol(Command, XmPlus, ref RdStr);
if (XmPlus.Class == 4) ret = DealWithFor(Command, XmPlus);
if (XmPlus.Class == 5) ret = DealWithKonica(Command, XmPlus, ref RdStr);
return ret;
}
＊if XmPlus.Type == Reg, The result of the reading will be placed in RdStr

## Slide 144: How to Use the API(Wolverine)
  Sample Code as below
XM_ExeWol_Util XmPlusUtil = new XM_ExeWol_Util();
XMUtil.MipiBridgeSelect(0x01);
XMUtil.SetFpgaTiming(0x33 ,0x11 ,0x13 ,0xff ,67 ,60);
XMUtil.SetMipiVideo(1334, 750, 60, 4, 255, 30, 2, 3, 6);
XMUtil.SetMipiDsi(2, 1000, "burst");
XMUtil.GpioCtrl(0x11, 0x00, 0x00);
XMUtil.BackLight_0_Ctrl(true, false); //Open BackLight
XMUtil.MipiWrite(0x05, 0x11);
Thread.Sleep(100);
XMUtil.MipiWrite(0x05, 0x29)
XMUtil.MipiRead(0x0a, 1, ref rdstr); // rdstr: 0x9c
XMUtil.ImageFill(0, 255, 0);

## Slide 145: Appedix

## Slide 146: Reset

## Slide 147: rst.trigger
rst.pol 0
rst.pol 1

## Slide 148: rst.set
rst.set 0xff 0
rst.reset
rst.set 0xff 1
rst.reset

## Slide 149: Instrument Connection

## Slide 150: Instrument Connection
1. Please Press “Scan” Button
2. Instrument Names showed in the List

## Slide 151: Instrument Connection
1. You can define Instrument Alias Name or use real name

## Slide 152: Instrument Connection
1. instr.xfer: Write ‘*IDN?’ to Scope and read
2. Show Reading Message from Scope

## Slide 153: Instrument Connection
1. instr.send: Send ‘*IDN?’ to Scope
2. instr.read: Read from Scope
3. instr.close: Close the Scope

## Slide 154: CA-210 Connection

## Slide 155: CA-210 Connection
Open CA210 CommPort
Setting Comm Setting
CommPort, 38400,7,E,2
1
2

## Slide 156: CA-210 Connection
Please Press ‘Remote’ Button

## Slide 157: CA-210 Connection
1. Open CA210 Comm Port Successfully

## Slide 158: CA-210 Connection
Send ‘Mes’ Command to CA210
After 200 ms , it will read the result from CA210

## Slide 159: K-80 Connection

## Slide 160: CA-210 Connection
Open K-80 CommPort
Setting Comm Setting
“K-80”,”COM8”
1
2

## Slide 161: K-80 Connection
It will read the bright or flicker from CA210

## Slide 162: 谢谢大家 !

## Slide 163: 指令說明
USB to EPP |  |  |  | FPGA |  |  |  |  |  | LCD Driver |  |  | 
command | addr strobe | data strobe |  | Register/addr | parameter | mode |  |  |  | interface | register | parameter | display data
EPPAddrWrite | V |  |  | 0x80 | display register and data write/read | addr. WR | FPGA to ext. LCD interface mode |  |  | CPU | function setting register | function setting parameter | display data Write/read
EPPDataWrite |  | V |  | 0x81 |  | data WR |  |  |  | RGB |  |  | 
EPPDataRead |  | V |  | 0x82 |  | addr. RD |  |  |  | SPI |  |  | 
EPPWriteCommand | V | V |  | 0x83 |  | data RD |  |  |  | I2C |  |  | 
WriteScanner |  | V |  | 0x8x | FPGA int. function(SRAM/FLASH/DCM…) |  |  |  |  | mipi |  |  | 
ReadScanner |  | V |  | 0x9x~0xFx | >=1 para. | FPGA int. register |  |  |  |  |  |  | 

## Slide 164: 指令說明
Epp address strobe | => | FPGA Register address set
Epp Data strobe write | => | FPGA Register Parameter write
example | LCD I/F | CPU 8bit[7:0]
 | USB to EPP | addr. | data |  |  | 
FPGA initial setting | EPPAddrWrite | 0x9x |  | FPGA timing setting |  | 
 | EPPDataWrite |  | 0xXX |  |  | 
 | EPPAddrWrite | 0xa0 |  | FPGA CPU I80/8bit[7:0] interface mode set |  | 
 | EPPDataWrite |  | 0x00 |  |  | 

## Slide 165: 指令說明
LCD command setting | EPPAddrWrite | 0x80 |  | FPGA to ext. I/F -> address write mode |  |  |  | 
 | EPPDataWrite |  | 0x0B | LCD command -> Read display pixel format |  |  |  | 
 | EPPAddrWrite | 0x83 |  | FPGA to ext. I/F -> data read mode |  |  |  | 
 | EPPDataRead |  | 0xXX | Read display pixel format |  |  |  | 
 | EPPAddrWrite | 0x80 |  | FPGA to ext. I/F -> address write mode |  |  |  | 
 | EPPDataWrite |  | 0x26 | LCD command -> Gamma Set |  |  |  | 
 | EPPAddrWrite | 0x81 |  | FPGA to ext. I/F -> data write mode |  |  |  | 
 | EPPDataWrite |  | 0x01 | Gamma Set -> GC0 |  |  |  | 
 | EPPAddrWrite | 0x80 |  | FPGA to ext. I/F -> address write mode |  |  |  | 
 | EPPDataWrite |  | 0x11 | LCD command -> sleep out |  |  |  | 
 | EPPDataWrite |  | 0x29 | LCD command -> display on |  |  |  | 

## Slide 166: 指令說明
LCD display data write | EPPAddrWrite | 0x80 |  | FPGA to ext. I/F -> address write mode |  |  |  |  | 
 | EPPDataWrite |  | 0x2C | LCD command -> memory write |  |  |  |  | 
 | EPPAddrWrite | 0x81 |  | FPGA to ext. I/F -> data write mode |  |  |  |  | 
 | EPPDataWrite | 擇一 | 0xXX | display data write, loop image size. Ex: 128x160x3 byte |  |  |  |  | Loop
 | WriteScanner |  | 0xXX |  |  |  |  |  | 
LCD display data read | EPPAddrWrite | 0x80 |  | FPGA to ext. I/F -> address write mode |  |  |  |  | 
 | EPPDataWrite |  | 0x2E | LCD command -> memory read |  |  |  |  | 
 | EPPAddrWrite | 0x83 |  | FPGA to ext. I/F -> data read mode |  |  |  |  | 
 | EPPDataRead | 擇一 | 0xXX | display data read, loop image size. Ex: 128x160x3 byte |  |  |  |  | Loop
 | ReadScanner |  | 0xXX |  |  |  |  |  | 

## Slide 167: Platform Function Call
2016/10/31
C# Instruction: XM_Comm_Base.XM_CommBase_DisWrite(0xf2, 1, 0xff, 1);
Function Call: GLWriteEPPDataPort , GLWriteEPPAddressPort
Flow:
      GLWriteEPPAddressPort(0x80)
      GLWriteEPPDataPort(0xf2)
      GLWriteEPPAddressPort(0x81)
      GLWriteEPPDataPort(0xff)

## Slide 168: Platform Function Call
C# Instruction:
      byte[] Val = { 0x80, 0xf2, 0x81, 0x61 };
      XM_Comm_Base. XM_CommBase_WriteCommand(Val, Val.Length);
Function Call: Epp2USB.UsbWriteCommand(WriteDataPtr, xbufLen);

## Slide 169: GL660 Function Call
C# Instruction:
      byte[] Val = { 0x11, 0x22,0x33, 0x44 };
      XM_Comm_Base.XM_CommBase_DisWrite(0x11, 1, Val, Val.Length);
Function Call:
    Epp2USB.UsbWriteScanner
Flow:
      GLWriteEPPAddressPort(0x80)
      GLWriteEPPDataPort(0x11)
      GLWriteEPPAddressPort(0x81)
      UsbWriteScanner (val)

## Slide 170: Gamma量測修改,Ongoing

## Slide 171: 修改Gamma量測方法
1. Date:2018/08/23
2. Let User to input sending commands for measuring Gamma.
3. 已經沒有R+ ….. B-的觀念，一個節點就是有P0~p6的點，256(Gray Level)*6, P0~P1535
4.使用預設Script，分成Write And Read Command

## Slide 172: 修改Gamma量測方法
[WRP0]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD4 P0[D9:D2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD4 P0[00,D1:D0,0010]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD5 P1[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD5 P1[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD6 P2[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD6 P2[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD7 P3[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD7 P3[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD8 P4[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD8 P4[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD9 P5[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD9 P5[000000,3:2]
[WRP1]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD4 P0[D9:D2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD4 P0[00,D1:D0,0010]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD5 P1[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD5 P1[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD6 P2[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD6 P2[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD7 P3[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD7 P3[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD8 P4[9:2]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD8 P4[000000,3:2]
mipi.write.hs 0x23 0x00 0x83
mipi.write.hs 0x29 0xD9 P5[1:0],P6[1:0],P5[1:0],P5[1:0]
mipi.write.hs 0x23 0x00 0x9E
mipi.write.hs 0x29 0xD9 P5[000000,3:2]

## Slide 173: 修改Gamma量測方法
[RGamma0]
mipi.write 0x23 0x80
mipi.read 0xD4 1 P0[d9:d4,000,d0]
mipi.write 0x23 0x9E
mipi.read 0xD4 2 P0[d1:d0]:P1[d1:d0]:P3[d1:d0]:P5[d1:d0],P0[d9:d2] ,……..

## Slide 174: Interface
Interface | Description |  |  |  |  | 
SPI | 0xa0,0x94 , 0x95, 0x96 |  |  |  |  | 
I80 | 0xa0=>0x00 |  |  |  |  | 
M68 | 0xa0=>0x08 |  |  |  |  | 
I2C | 0xa0 |  |  |  |  | 
resetH | 0x90 |  |  |  |  | 
fgpa.set |  |  |  |  |  | 
fpga.set | Pll_Bank_En | EPP_EN | I/F_Mode1 | I/F_Mode2 | DCM_M | DCM_D

## Slide 175: Interface

## Slide 176: Interface Setting
fpga.set
cpu.set
spi.set
i2c.set
spi.write
i2c.write
cpu.write
Rgb.image.fill
Rgb.image.show

## Slide 177: PLL設定
1.SSD2828 Bank Enable and Mode Set
  If Bank =1 and Video Mode =1 , PLL Enable(Reg:0xF3)
  2. IfA0[5:3]:010 or 101 , PLL Enable(Reg:0xF3)

## Slide 178: Details
1.SSD2828 Bank若先Enable,則其他DataPath先Disable

## Slide 179: SPI

## Slide 180: SPI
fpga.write 0xa0 0x18
fpga.write 0x95 0x22
fpga.write 0x96 0x44
fpga.write 0x94 0x00
fpga.write 0x90 0x03
fpga.write 0x90 0x02
cpu.addr.write 0xA5
fpga.write 0x90 0x03
fpga.write 0x90 0x02
cpu.data.write 0x5A
fpga.write 0x90 0x03
CS
SCK
SDI
D/C

## Slide 181: SPI

## Slide 182: Bug

## Slide 183
Gpio.set reg , Shutdown